____________________________________________________________________________

Status of code / additional notes
Points / descriptions to check
Priority to check
Choice (to re-visit later or after writing code in full)
Checks
Code snippets

____________________________________________________________________________

Text file with information about Deltas (COMPLETE)

Table of:
Delta, Mc_SLN, Mp_SLN, sigma_LN, sigma_SLN, alpha_SLN, alpha_CC3, beta

Isatis runs

Unmodified version
Monochromatic MF

____________________________________________________________________________

START OF PROGRAM:

Imports:
- numpy
- matplotlib.pyplot
- matplotlib

Plotting style code

___________________________________________________________________________
OUTLINE:
- Methods:
  - To evolve phi (or psi, if possible)
    - Check: for log-normal, Fig. 2 of MP ‘22
  - To calculate psi(M, t) [if necessary]
  - alpha_eff_extracted(M_init): Result for alpha_eff, extracted from Fig. 1 of Mosbech & Picker (2022).
  - mass_evolved(M_init_values, t): Find the PBH mass at time t, evolved from initial masses M_init_values.
  - constraint_Carr(): Calculate constraint on f_PBH for an extended mass function, using the method from 1705.05567.

____________________________________________________________________________

METHODS:

constraint_Carr(mc_values, m_delta, f_max, psi_initial, params, t):
"""
Calculate constraint on f_PBH for an extended mass function, using the method from 1705.05567.

Parameters
----------
mc_values : Array-like
Characteristic PBH masses (m_c for a (skew-)lognormal, m_p for CC3).
m_delta : Array-like
Masses at which constraints for a delta-function PBH mass function are evaluated..
f_max : Array-like
Constraints obtained for a monochromatic mass function.
psi_initial : Function
Initial PBH mass function (in terms of the mass density).
params : Array-like
Parameters of the PBH mass function.
evolved : Boolean
If True, calculate constraints using the evolved PBH mass function.
t : Float
Time (after PBH formation) at which to evaluate PBH masses.
Returns
-------
f_pbh : Array-like
Constraints on f_PBH.

"""

If the constraints are only calculated at PBH masses greater than 1e18g, ignore the effect of evaporation:
if min(m_delta) > 1e18:
evolved = False

f_pbh = []

m_init_values_input = np.concatenate((np.arange(m_star, m_star*(1+1e-11), 5e2), np.arange(m_star*(1+1e-11), m_star*(1+1e-6), 1e7), np.logspace(np.log10(m_star*(1+1e-4)), 18, 500)))
m_values_input = mass_evolved(m_init_values_input, t)

for m_c in mc_values:

if evolved:

- Find the evolved mass function at time t after PBH formation
  psi_initial_values = psi_initial(m_init_values_input, m_c, *params)
  psi_evolved_values = psi_evolved_normalised(psi_initial_values, m_values_input, m_init_values_input)

Interpolate the evolved mass function at the masses that the delta-function mass function constraint is calculated at
m_values_input_nozeros = m_values_input_nozeros[psi_evolved_values > 0]
psi_evolved_values_nozeros = psi_evolved_values[ psi_evolved_values > 0]
psi_evolved_interp = 10**np.interp(np.log10(m_delta), np.log10(m_values_input_nozeros), np.log10(psi_evolved_values_nozeros), left=-100, right=100)

integral = np.trapz(psi_evolved_interp / f_max, m_delta)
if integral == 0 or np.isnan(integral):
f_pbh.append(10)
else:
f_pbh.append(1/integral)

else:
integral = np.trapz(psi_initial(m_delta, m_c, *params) / f_max, m_delta)
if integral == 0 or np.isnan(integral):
f_pbh.append(10)
else:
f_pbh.append(1/integral)
return np.array(f_pbh)

Tests

For evolved MFs, in MP22_Fig4_reproduction_minimal.py

See final cell
- Test of method constraints_Carr() [constraint_evolved in the previous cell and constraint_evolved_CC should match exactly].
- Uses the Fermi-LAT data from Lacroix et al. (2015), monochromatic MF constraint calculated using CL=0 in isatis_reproduction.py

Compare results for unevolved MFs, for other constraints

511 keV line constraints (Korwar & Profumo (2023))

Galactic photon constraints (Isatis)

Side tests / extra checks

Practicalities of using normalised and non-normalised extended MF calculation

Korwar & Profumo (2023)

When calculating the normalised MF, the results are divided by an integral of the mass function over the mass. This means that the amplitude of the normalised MF is sensitive to the mass range used for integration. If the mass range is too small, then the amplitude of the normalised MF is too large.

In the method constraint_Carr(), by default I am calculating the normalised MF using the mass range at which the delta-function MF constraint is calculated.

The maximum mass at which the delta-function MF constraint is estimated is at ~3e17g.

To compare the accuracy of the normalised MF to the unnormalised MF:
- Compare the evolved mass functions to the initial mass functions at masses where the effects of evaporation are negligible (M >~ 1e15g).

In practice, I find that for M_c >~ 1e16g, with a maximum value of M = 3e17g, the prediction of the unnormalised MF is considerably better than that of the normalised MF (for Delta = 5, with M_p = 1e17g, the difference from the initial mass can be a factor of 10 at M>3e15g!) [shown in figure below]

Ways to address this:
- Use the normalised MF, but calculate the normalisation integral over a wider range of masses (e.g. for a maximum mass M=1e21g, the fractional difference approaches ~3e-4 at M > 3e15g for the CC3 with Delta=5.0 and M_p = 1e17g) [done]
- + Closer to “correct”, from what I understand of the method from Carr et al. (2017)
- - Slightly more complicated to calculate

- Use the unnormalised MF
  - + Simpler, requires no additional calculations
  - - I don’t think it is exactly correct [decided against this]

Changes:
Modify the following code line in constraints_Carr():

        m_init_values_input = np.concatenate((np.arange(m_star, m_star*(1+1e-11), 5e2), np.arange(m_star*(1+1e-11), m_star*(1+1e-6), 1e7), np.logspace(np.log10(m_star*(1+1e-4)), np.log10(max(m_delta)), 500)))

to

        m_init_values_input = np.concatenate((np.arange(m_star, m_star*(1+1e-11), 5e2), np.arange(m_star*(1+1e-11), m_star*(1+1e-6), 1e7), np.logspace(np.log10(m_star*(1+1e-4)), np.log10(max(m_delta))+4, 500)))

Number of steps to evaluate MF at
- So far, have been evaluating the evolved MF at 500 masses for interpolation and calculating the extended MFs
- Compare agreement with initial MF at M >~ 1e15g using: 500, 1000, 5000 steps, with the maximum mass M_max = 3e21g

500 steps

1000 steps

5000 steps

Results:
- The difference is small (sub-percent) for all numbers of steps I tried (varying the number of steps by an order of magnitude varies the fractional difference by a factor of ~2) => the mass range is much more significant than the number of steps used
- The absolute value of the difference is minimised using 1000 steps => use 1000 steps

Check effects on MP22_Fig4_reproduction_minimal.py results
- Changing from 500 to 1000 steps (to 5000 steps) has a sub-percent effect on the results for M_c >~ 4e15g (for a mass range up to 1e22 g in the calculation)
  - At smaller M_c, the difference can reach up to 65%, and becomes consistently worse as M_c decreases
- Changing the upper limit of the mass range from 1e18g to 1e22g (using 1000 steps) leads to a sub-percent difference for M_c >~ 5e15g
  - At smaller M_c, the difference can reach up to 60%, and becomes consistently worse as M_c decreases

It appears unlikely that these changes will have a significant effect on the results in the mass range that I am interested in.

Check of method constraint_Carr() when reproducing constraints
Compare results obtained with the unevolved MF constraints

In the following plots:
- Solid line: the “old” calculations that I calculated with the old version of the method constraint_Carr()
- “x”: Calculated using the new version of the method constraint_Carr(), with the argument evolved=False
- “+”: Calculated using the new version of the method constraint_Carr(), with the argument evolved=True and t=0

Korwar & Profumo (2023)

Delta = 0.0: difference between solid line, “x” and “+” is < 1% at all peak masses m_p plotted that I’ve checked
Delta = 5.0: difference between solid line and “+” is very small, while the difference between the solid line and “x” is approximately 10% for all three mass functions at M_c <~ a few times 10^16 g, and is visible upon zooming in

To understand:
How does a sub-percent (< 1e-4) difference in the mass function lead to a ~10% difference in the results for f_PBH at small M_c?

Possibility:
- Currently, the minimum and maximum masses I am calculating the masses at are ~7e14g and ~3e21g
  - For M_c close to 1e16g, this includes considerably more of the mass function at higher masses than at lower masses [for the LN and SLN, M_c > M_p, so the lower range of masses below M_c should be wider (in log space) than the range above (in log space)
  - It may be that including a wider range at lower masses would bring the results into closer agreement. For the evolved MF this would be less of a problem, since the minimum masses close to ~7e14g will be “stretched” due to evaporation into a wider range of PBH masses at late times
To check:
Change the following line of code in the method constraints_Carr() in preliminaries.py

    m_pbh_values_formation = np.concatenate((np.arange(m_star, m_star*(1+1e-11), 5e2), np.arange(m_star*(1+1e-11), m_star*(1+1e-6), 1e7), np.logspace(np.log10(m_star*(1+1e-4)), np.log10(m_delta_max_KP23)+4, 1000)))

to

        m_init_values_input = np.sort(np.concatenate((np.logspace(np.log10(min(m_delta)), np.log10(m_star), 1000), np.arange(m_star, m_star*(1+1e-11), 5e2), np.arange(m_star*(1+1e-11), m_star*(1+1e-6), 1e7), np.logspace(np.log10(m_star*(1+1e-4)), np.log10(max(m_delta))+4, 1000))))

Results:a
“x” (setting t=0 in the calculation) agrees with “+” and solid line, even at M_c ~ 1e16g

Comment:
This change is likely to be unhelpful or irrelevant when actually evolving the mass function, since no PBH with formation M_i < M_* will contribute to the constraint today. So the extra array is unnecessary extra computation.

(27/7): Updated sanity check
For simplicity, I am making the following changes to the first cell of plot_constraints_tests.py:
- Remove the Galactic Centre photon constraints calculated using Isatis
  - These are already tested by comparing the results obtained using the unevolved MF and t_initial
  - I have concluded that the “full” calculation (calculating the constraint in each energy bin and taking the minimum) is too computationally expensive and not worth doing, since a more approximate calculation is still reasonably accurate
    - Therefore, this is unnecessary duplication
    - see 24/7 entry: Check / correction : unevolved MF with no extrapolation, comparison between ‘full’ and approximate calculations)
- For the KP ‘23 511 keV line constraints, don’t include the ‘extrapolated’ case
  - Reason: this removes a source of ambiguity and confusion
    - In the old data sets, I used extrapolation to estimate the delta-function MF constraint down to 1e15g. In the new data, extrapolation can refer to either this case or extrapolating to lower masses (1e11g)
  - Reason: it is unnecessary (since I can calculate the constraint again with no extrapolation at all)

Results
- Difference between the unevolved MF results and the old calculation is not visible in any case
- Difference between unevolved MF results and t_initial results is not visible in most cases
  - The maximum difference is ~2.5%, occurring for the SLN MF with Delta = 5.0 at the lower end of the asteroid-mass window
  - (I expect a small difference between the t_initial and unevolved MF results since the former uses interpolation, while the latter is calculated directly at the PBH masses, and should match the old results exactly, which is what is seen.)
Conclusion
The sanity check is passed excellently.

To do:
- Move the relevant methods appearing in MP22_Fig4_reproduction_minimal.py to a different code file with the methods required to calculate extended MF constraints
- Check the method constraint_Carr for an unevolved MF, by comparing the results to the unevolved MF constraints
  - Check by setting evolved = False as an argument
    - Korwar & Profumo (2023)
    - Galactic Centre photon constraints from Isatis: check
  - Check by setting t=0 as an argument
    - Korwar & Profumo (2023)
    - Galactic Centre photon constraints from Isatis: check

- Calculate the evolved MF constraint (mean value)
  - Korwar & Profumo (2023)
    - One check to complete: Delta = 5 results for the first sanity check with unevolved MFs
  - Galactic Centre photon constraints

Calculate the effect of uncertainties in the constraints

  - Korwar & Profumo (2023)
    - Try with different power-law extrapolations down to M~1e11g
      - Contribution from secondary emission of positrons will increase the total flux emitted from PBHs, therefore tightening the constraint compared to the case considering only primary emission. The power-law at M <~1e15g will be steeper than the ~M^2 behaviour seen at larger masses
      - Try power law slopes 2, 3 and 4

  - Galactic Centre photon constraints
    - Try with different power-law extrapolations down to M~1e11g
      - Below M~1e13g, the Hazma code becomes unreliable at calculating the constraint. Try a range of possibilities:
        - Flat constraint (power-law slope = 0)
        - Power law slopes of 2 (reasonable, given the behaviour of the constraint at m > 1e13g, and the behaviour of the total photon emission rate as a function of mass) and 4

- MeV gamma-ray telescopes (modelled off GECCO results from Fig. 9 of Coogan et al. (2023))
  - Try with different power-law extrapolations between 1e11g – 1e15g
    - Results not shown for the delta-function MF constraint below M = 1e15g. Since this constraint is also obtained from the photon emission from PBHs, test the same slopes as the existing Galactic Centre photon constraints, i.e.
      - Flat constraint (power-law slope = 0)
      - Power law slopes of 2 (reasonable) and 4 (extreme)

Power-law extrapolations in f_max(M)
Aim: test the effect on constraints on f_PBH just below the lower end of the asteroid-mass window by comparing results obtained using different functional forms of f_max(M) in a mass range where the the constraints calculated for f_max(M) may not be reliable.

Korwar & Profumo (2023)

Background
- Currently, extrapolating f_max(M) in the mass range 1e15 – 1e16g with a power law in M^2:
  - Justification: Since the integrated emission of the total positron emission from PBHs is well-fit by a power law M^{-1} (a factor of 1/M appears from converting the mass density of PBHs into a number density when calculating the J-factor, leading to an approximate behaviour of 1/M^2 in the flux of 511 keV photons resulting from PBH emission, or ~M^2 in the constraint itself).
  - Plot of the total emission shown is integrated over the energy range (511 keV – 5 GeV), with the upper limit of 5 GeV corresponding to the maximum value calculated using Hazma.

  - Plot of the positron emission spectrum integrated over the energy range (511 keV – 1e5 GeV), with the upper limit of 1e5 GeV corresponding to the maximum value calculated using PYTHIA.
    - PYTHIA calculations valid at E >~ GeV, see Sec. 2.4 of 2207.03266
    - CHECK: which forms of the fM tables are being used here? Does this make a difference?
      - I have tried both the old versions and the QCD-scale corrected ones (setting the u, d and s quark masses to the QCD confinement scale), and it does not seem to make a difference.

- Below M = 1e15g, secondary emission of positrons becomes significant, and the f_max ~ M^{-2} modelling is likely to break down
  - From Fig. 1 of CKSY ‘16 (1604.05349), the increase in emission might be associated with the emission of muons by the BH

- To extrapolate below M = 1e15g, use a power law dependence in f_max(M)
  - Match all the f_max(M) at M = 1e15g
  - Use a power-law in M that produces a more stringent constraint
    - Justification:
      - The constraint goes as [(dN_e/dt) / M]^{-1}
        - Why? Since the luminosity from PBHs is proportional to PBHs,
          - f_PBH = observed luminosity / PBH luminosity(f_PBH=1)
      - dN_e/dt decreases faster than 1/M at M <~ 1e15g
        - E.g. if dN_e/dt ~ 1/M^2, constraint goes at f_max ~ [1/M^3]^{-1} ~ M^3
  - From the plot obtained using Hazma, dN_e / dt appears to have a slope of between -1 and -2 in the mass at M <~ 1e15g

Below 1e15g, compare the results obtained with power-law slopes below 1e15g and power-law slopes of (2, 3 and 4)

Results:

Delta < 5:
Difference between the different power law curves in f_max(M) is insignificant at the lower end of the asteroid-mass window
Delta = 5, compare f_PBH at the lower end of the asteroid-mass window
- LN
  - f_PBH(PL slope = 3) a few percent stronger than the constraint for f_PBH(PL slope = 2)
  - f_PBH(PL slope = 4) ~ 30% stronger than the constraint for f_PBH(PL slope = 2)
  - f_PBH(PL slope = 4) ~ 30% stronger than the constraint for f_PBH(PL slope = 3)
- SLN
  - f_PBH(PL slope = 3) ~ 1% stronger than the constraint for f_PBH(PL slope = 2)
  - f_PBH(PL slope = 4) ~ 16% stronger than the constraint for f_PBH(PL slope = 2)
  - f_PBH(PL slope = 4) ~ 15% stronger than the constraint for f_PBH(PL slope = 3)
- CC3
  - f_PBH(PL slope = 3) a few percent stronger than the constraint for f_PBH(PL slope = 2)
  - f_PBH(PL slope = 4) ~ 40% stronger than the constraint for f_PBH(PL slope = 2)
  - f_PBH(PL slope = 4) ~ 40% stronger than the constraint for f_PBH(PL slope = 3)

Sanity check [passed]:
- When Delta=5, using a steeper f_max(m) at m < 1e15g has almost the same effect for the LN and CC3 MFs, but a smaller effect for the SLN MFs:
  - Reasoning
    - The impact of changing the power law at m < 1e15g will be sensitive to the low-mass tail behaviour of the fitting functions
    - From Fig. 5 of Gow et al. (2022) [2009.03204], the low-mass tail of the SLN and CC3 MFs are larger than that from the SLN
    - Since it is not clear whether the peak masses are exactly the same in Fig. 5 of Gow et al. (2022), I also plotted the three mass functions in a case where the peak masses are definitely equal (see the cell “Plot the mass function for Delta = 5.0, showing the mass range relevant for the Subaru-HSC microlensing constraints.” in preliminaries.py (shown below)
      - Comment: at a peak mass of ~1e18g, the lower bound of the plot shown below will correspond to ~1e16g, which is well above the mass at which evaporation starts to become significant
      - Re-plot for evolved MFs?

To think about:
- Other sanity checks??
- Plot result where there is no constraint below 1e16g?
- What is a reasonable value for the power-law (use the behaviour of dN_e / dt to justify roughly, maybe consider using PYTHIA at larger energies to get an estimate?)
  - Plotting the integrated spectrum of electrons/positrons emitted by PBHs from Hazma and PYTHIA implies the slope of the integrated electron emission spectrum lies between 1/m and 1/m^2
  - From Eq. (3.1) of Korwar & Profumo (2023)
- Include evolved MF w/o constraint below 1e16g?

Sanity check:
- Compare results obtained using no constraint below 1e16g with the evolved and unevolved MF constraints
- To check
  - The unevolved and evolved MF constraints should match closely, since at M > 1e16g the effects of evaporation are negligible. This is the case
- Comparison to the evolved MF constraints shows the following:
  - Delta < 5:
    - Evolved MF vs unevolved MF has a very small effect at the lower end of the asteroid mass window
  - Delta = 5:
    - LN:
      - f_PBH(PL slope = 2 or 3) ~ 40% stronger than f_PBH(not including m < 1e16g)
      - f_PBH(PL slope = 4) ~ 60% stronger than f_PBH(not including m < 1e16g)
    - SLN:
      - f_PBH(PL slope = 2 or 3) ~ 30% stronger than f_PBH(not including m < 1e16g)
      - f_PBH(PL slope = 4) ~ 40% stronger than f_PBH(not including m < 1e16g)
    - CC3:
      - f_PBH(PL slope = 2 or 3) ~ 40% stronger than f_PBH(not including m < 1e16g)
      - f_PBH(PL slope = 4) ~ 70% stronger than f_PBH(not including m < 1e16g)

As well as a sanity check, this gives some idea of how significant the behaviour of the delta-function MF constraint from Korwar & Profumo (2023) is at m <~ 1e15g

  - Justification: At M~1e13g, the PBH temperature is ~1 GeV. The maximum primary particle energy simulated by Hazma is 5 GeV, so the results are likely to not be reliable at smaller masses
- To do

Sanity check:
Plot f_PBH for the unevolved MFs, using f_max estimated down to M=1e11g using a power-law extrapolation.

What I’d expect to see:
- Closest agreement between the unevolved MF and evolved MF results at larger peak masses m_p, with some difference appearing at smaller masses
- The constraints obtained with an unevolved MF may be less stringent, since there is no low-mass tail going as M^2 in f_max

Initial results are surprising:
- Delta = 5.0
  - Unevolved LN results less stringent (or shifted to smaller masses) than the evolved MF constraints
  - Unevolved CC3 and SLN constraints more stringent (or shifted to larger masses) than the evolved MF constraints
  - t_init and “evolved=False” results appear to agree closely for two of the power-law slopes but not the third
- Delta = 1.0, 2.0
  - Unevolved LN and SLN results more stringent (or shifted to larger masses) than the evolved MF constraints
  - Unevolved CC3 results less stringent (or shifted to smaller masses) than the evolved MF constraints
  - t_init and “evolved=False” results appear to agree closely for two of the power-law slopes but not the third
- Delta < 1.0:
  - Unevolved LN results appear to agree reasonably well below M_p ~ 1e17g, and are slightly tighter than the evolved MF results at larger m_p
  - Unevolved SLN results more stringent (or shifted to smaller masses) than the evolved MF constraints
  - Unevolved CC3 results less stringent (or shifted to larger masses) than the evolved MF constraints
  - t_init and “evolved=False” results appear to agree closely for two of the power-law slopes but not the third

Following discussion with Anne in a meeting (19/7), no longer pursuing this as it is not clear precisely what it would be checking.

NOTE: I tried re-doing the first sanity check and found very surprising results for Delta=5 (smaller Delta results are fine). Come back to this.

Galactic Centre photon constraints (estimated using the hadronisation code Hazma)
- The results I have are likely to break down below M ~ 1e13g
  - Compare results obtained with different functional forms of f_max(M), evaluated down to M=1e11g
    - Match all the f_max(M) with the value calculated using Isatis (or isatis_reproduction.py) at M = 1e13g
    - Use
      - power-laws with slopes of (0, 2, 4)
      - No constraint below 1e13g

Logic of calculation:

1. Load data for f_max(M) from each instrument (“fPBH_GC_full_all_bins_%s_monochromatic_wide.txt” (indexed by i) (%s = name of the instrument and paper the observational data is from)
Create empty array for constraints at each value of the characteristic mass (for LN and SLN) or peak mass (for CC3)

2. Loop over values of the characteristic mass / peak mass
- Set mc_values to a single-entry array with value equal to the value of the characteristic mass / peak mass, mc_values_input
- Create an empty array of constraints evaluated at that m_c, from each energy bin of the instrument, energy_bin_constraints_{LN, SLN, CC3}

3. Loop over energy bins within the data set (indexed by k)
- Load data for f_max at M > 1e13g
- Extrapolate data for f_max using a power law in the mass range 1e11g < M < 1e13g
- Set each the constraint f_max equal to the k’th entry of the data file
  - Truncate the loaded constraint f_max to a mass range corresponding to M > 1e13g
  - Extrapolate the behaviour of f_max down to 1e11g using a power-law fit, matching to the loaded data for f_max at M=1e13g
- Calculate the constraint using constraint_Carr from each energy bin at that m_c, for each extended MF
- Append that constraint to the array of constraints evaluated at that m_c, energy_bin_constraints_{LN, SLN, CC3}

Simpler, (hopefully faster) calculations
1. Load data for each instrument (indexed by i)
- Find the corresponding f_max(M) for each instrument f_max_loaded = f_max_Isatis[i]
- Calculate extended MF constraints from each instrument, at each m_c

To sort:
- Unphysically small values in f_max

Diagnosis:
- Unable to reproduce the close agreement at t=0 and t=t_init with the “old” data.

Modifications to bring closer to original:
- In preliminaries.py, change m_init_values_input from:
        #m_init_values_input = np.sort(np.concatenate((np.logspace(np.log10(min(m_delta)), np.log10(m_star), 1000), np.arange(m_star, m_star*(1+1e-11), 5e2), np.arange(m_star*(1+1e-11), m_star*(1+1e-6), 1e7), np.logspace(np.log10(m_star*(1+1e-4)), np.log10(max(m_delta))+4, 1000))))

to

        m_init_values_input = np.concatenate((np.arange(m_star, m_star*(1+1e-11), 5e2), np.arange(m_star*(1+1e-11), m_star*(1+1e-6), 1e7), np.logspace(np.log10(m_star*(1+1e-4)), np.log10(max(m_delta))+4, 1000)))

Problems with older versions from GitHub:
- Using mc_values in place of m_c, which meant that all of the output f_PBH (for a given instrument) had identical values for all m_c
- Not looping over the energy bins of the instrument. Instead, calculating only the COMPTEL constraint

23/7
Initial results of test comparing GC photon constraints (calculated using Isatis) obtained for:
- Unevolved MF (controlled with the boolean ‘evolved’ in constraints_Carr)
- Results obtained before June 2023 (which use the unevolved MFs)
- ‘Evolved’ MFs evaluated at t=0 (i.e. the arguments ‘evolved = True, t=0’ in constraints_Carr)

Unevolved MF vs results obtained before June 2023:
- Delta < 5.0: Sub-percent differences at the lower end of the asteroid-mass window
- Delta = 5.0: Differences of ~10% (SLN) and ~40% (CC3) at the lower end of the asteroid-mass window
  - In both cases the more recent calculation predicts tighter constraints than the older results

- Understanding differences when Delta = 5.0
  - More stringent constraints: likely that the ‘old’ calculation is underpredicting the results?
  - If difference is due to the monochromatic MF calculation:
    - Must only be significantly affecting the widest mass functions, so it impacts one of the tails (presumably low
  - If difference is due to the extended MF calculation:
    - Since the CC3 has larger values in the low-mass tail than the SLN, it may be that the contribution from low-mass PBHs is underestimated. Lower masses of delta-function MF constraint too low for

I am trying the test with the ‘evolved’ MF evaluated at t=0. However, this takes hours to run, so it seems impractical to use.

Instead, use f_max as the delta-function MF constraint from each instrument. For a log-normal MF at least, I found this agrees reasonably well with the exact calculation (calculating the constraint from each energy bin of each instrument and taking the minimum). I find the maximum differences are

The difference is likely smaller than the uncertainties in the constraint, so this approximation should be reasonably good, and saves time.

24/7

f_max as delta-function MF constraint (“approximate”)

Test: comparison of unevolved MF with t=0 results
- Very close agreement, for all Delta at all m_p (visually indistinguishable)

Test: comparison of results using f_max as the delta-function MF constraint from each instrument (“approximate”) to results obtained using each separate energy bin as f_max (“exact”) [at t=0 / unevovled]
- Approximate more stringent than exact
- Focusing on the lower end of the asteroid-mass window, the maximum difference is a factor of approximately 2, which is seen for Delta = 2 and Delta = 5

Check the correct (most recent) data is being loaded by comparing the values of the variables to those from the most recently produced .txt files.

Extrapolating MF to m <~ 1e13g using power-law extrapolation (GC photons)

Background
I do not trust the delta-function MF constraints (obtained using Hazma) for m <~ 1e13g
Reason: For m <~ 1e13g, the PBH temperature T >~ 1 GeV, which is of the same order as the maximum primary particle energy that Hazma can use when calculating hadronisation tables
Therefore, in the delta-function MF constraint I am extrapolating below 1e13g using a power-law

Reasonable power laws
Plot of the photon emission spectrum integrated over the energy range (511 keV – 1e5 GeV), with the upper limit of 1e5 GeV corresponding to the maximum value calculated using PYTHIA.

- Relating this to the power-law slope
  - Eq. (7) of Auffinger (2022) [2201.01265] gives d\Phi / dE ~ Q~\gamma / M
  - Eq. (11) gives f_PBH ~ 1 / int(d\Phi / dE) ~ 1 / (int(dN / dt) / M)
- Note: Unlike the Korwar & Profumo (2023) constraint, the Isatis constraint is calculated by integrating the total photon spectrum over a limited energy range corresponding to each energy bin.
  - Therefore, this plot is not showing the exact result used in the calculation of the Isatis constraint

- From this plot, reasonable power-law slopes in f_max appear to be:
  - Between 2 and 3 (corresponding to the orange and grey dotted lines, respectively)

- Further motivation:
  - Eq. (12) of Auffinger (2022) [2201.01265] gives an empirical power-law fit to the constraints with a power law exponent of 2.8, suggesting a slope of ~3 should provide a reasonable fit.

- As extreme cases, also consider:
  - 0, 4

Initial results for f_PBH
Evolved MF, “approximate” calculation, f_max extrapolated using power law below 1e13g.

Initial findings:
- All power law slope extrapolation results agree very closely (within a percent level), for all Delta and all MFs, even at the lower end of the asteroid-mass window.

Checks

In the calculation, the delta-function MF masses are 1000 values logarithmically spaced between 1e11g and 1e21g. Check that the data loaded using load_results_Isatis(modified=True) corresponds to this mass range by

- i) Check it is not the ‘wide’ mass range in the method load_results_Isatis, [passed]
  - Default arguments are load_results_Isatis(mf_string="mono_E500", modified=True, test_mass_range=False, wide=False)
- ii) Check that the plot of f_max matches that of Auffinger (2022) Fig. 3 (modulo the differences due to Fig. 3 not including the highest-energy bin)
  - Plot f_max(m), showing the extrapolated results below 1e13g, but narrow in on the mass range that is shown in Fig. 3 of Auffinger (2022):
  - For the most part, the results appear consistent with those in Fig. 3 of Auffinger (2022)

Re-run the following cases, to check that the results are identical those I obtained earlier today:
- Unevolved MF
  - Checked a couple of different instruments, MFs and values of Delta. Compared a few values. All identical with those uploaded to GitHub prior to making the changes here.
- t_initial = True
  - Checked a couple of different instruments, MFs and values of Delta. Compared a few values. All identical with those uploaded to GitHub prior to making the changes here.

Is the “envelope” method working correctly? [passed]
- To check, print the constraint on f_PBH for the LN at the smallest peak mass, for each instrument
- Check that this is the value of the constraint from the actual .txt file for one or two instruments at the smallest peak mass
- Compare to the output of the “envelope” method

Are the characteristic mass values m_c the same as in the script “GC_constraints_Carr.py”? [passed]
Yes

Understanding / sanity checking results

Galactic Centre photon constraints (with power-law extrapolation below 1e13g in delta-function MF constraint)

In brief, the results obtained using different power-law extrapolations (both reasonable and more extreme) agree excellently for peak masses m_p >~ 1e15g.

I've attached a plot of constraints for f_PBH, calculated for evolved extended mass functions where the delta-function MF constraint follows a power-law below a mass m = 1e13g, plotted against the peak mass.

- A constraint is calculated for each of the data sets used in Isatis (COMPTEL, Fermi-LAT, etc.). At each peak mass, I plotted the most stringent constraint out of the constraints obtained from each of the data sets.
- The top-left panel shows the delta-function mass function constraint f_max. I showed the constraints obtained using power-law exponents of 2 and 3 (as reasonable values) as well as extreme exponents of 0 (f_max constant at masses below 1e13g) and 4.
In the relevant range of peak masses m_p, there is excellent agreement between the results obtained using different power-law slopes in f_max below 1e13g. I think this seems plausible, since the mass at which the delta-function MF constraint f_max changes is very small compared to the peak masses of the mass functions.

In these calculations, I’m setting the delta-function mass function constraint to the constraint obtained from each instrument. I think I previously mentioned that this calculation (which I’ll call ‘approximate’) does not give the same results as the ‘full’ calculation, in which the constraint is calculated by requiring that the photon flux predicted from a PBH population (with an extended MF) does not exceed the measured flux in each energy bin of each instrument.

Comparing the full and approximate calculations using the unevolved versions of the mass functions, the difference between the results is no more than a factor of a few. Implementing the ‘full’ calculation when including the extrapolation of the delta-function mass function constraint takes 20+ hours to run, compared to a few minutes for the ‘approximate’ calculation. Given this and the relatively small difference from the approximate calculation when using the unevolved MFs, to me it seems more reasonable to use the approximate calculation.

Observation:
- The difference between the results for different power-law slopes starts to become visible between 1e14g – 1e15g when Delta = 0.0. For Delta = 5.0, the difference in the results remains negligible at m_p ~ 1e14-1e15g. This seems surprising.
Delta = 0.0: at m_p = 1e14g, difference is largest for CC3 (40-50%), SLN (12-14%) and smallest for the LN (9%)
- Plotting the MF:
- Consider m < 1e13g (where the constraint to the different power laws):
  - Delta = 0:
    - psi_N ~ 1e-18 (LN) [<< peak] , ~ 1e-16 (SLN) [close to peak], ~1e-15 (CC3) [close to peak]
  - Delta = 5:
    - psi_N ~ 1e-22 [<< peak]

Conclusion:
- For Delta = 5, when m_p = 1e14g, the mass function is largest at masses above where the power-law extrapolation becomes significant
- For Delta = 0, when the peak mass of the unevolved MF m_p = 1e14g, for the SLN and CC3, the mass function is large (compared to the peak of the evolved MF), at around m_p ~ 1e13g, where the effects of the different power-laws is significant. The reason the peak is at a lower mass is due to the evolution of the MF

Check / correction : unevolved MF with no extrapolation, comparison between ‘full’ and approximate calculations
- “Full”: require PBH flux does not exceed the measured flux for each energy bin of each instrument
- “Approximate”: use the delta-function MF constraint for each instrument as f_max in Isatis
- Compare “full” calculation and “approximate” calculation, when using the GC photon constraints with no extrapolation below 1e13g, and unevolved MFs.
The “full” calculation results are old results I had from before June 2023.

Results:
- “t_init” (i.e. evolved MF evaluated at t=0) “+” matches closely with the full (solid line)
- “unevolved” (using the unevolved MF) “x” appears shifted to significantly larger peak masses than the others
This affects the CC3 MF at all values of Delta, at all peak masses
- The apparent shift is largest for Delta = 5, and decreases as Delta gets smaller

Checks:

- Do the unevolved results agree with the others reasonably well if I plot m_p * np.exp(-sigmas_LN[j]**2) or
m_p * np.exp(-sigmas_LN[j]**2/2).
No

- Does the data actually match the most recent output?
- Print a few results for the log-normal case (Delta = 5), and compare to the most recent runs of GC_constraints_Carr.py
  - “Unevolved” MF: Yes
  - “t_init” MF: Yes
- Interestingly, the two match very closely with each other (typically to the third or fourth significant figure). This implies that the issue arises when plotting the constraints, rather than calculating them

- Found error:
I was plotting the SLN MF constraints instead of the CC3 constraints for the unevolved “x” case.

Difference between approximate and full calculations:
For all the cases I’ve checked, the difference is no larger than a factor of a few (< 3) at the lower end of the asteroid-mass window.

- The approximate results are always equally strong, or more stringent, than those from the full calculation
- The differences are largest for wider mass functions Delta = 2, 5
- The differences don’t depend simply on the peak mass – differences of around 2-3 can appear at a wide range of peak masses, not just around the lower end of the asteroid-mass window or at much smaller values
  See the pictures in “Jul 23 / 25-7_fPBH_full_approx_calculation_comparison_Delta={}_{}”

Microlensing constraints: power law extrapolation check

Background:
- Bellomo et al. (2018) indicate that one of the advantages of their method is that it includes the whole range of PBH masses from the delta-function MF constraint f_max, not only where f_max < 1
- So far, I have been calculating extended MF microlensing constraints using the delta-function MF microlensing constraints from Croon et al. (2020), which are only shown for f_max < 1
- I am interested to check how different behaviours of f_max at m <~ 1e22g affect the results on the extended MF constraints

Approach:
- Try power-law extrapolations with exponents -2 and -4, at masses 1e18g < m < 9e21g in the delta-funciton MF constraint
These are slightly steeper than the constraint appears to go at m <~ 1e22g. However, I would expect the constraint to become reasonably steep much below ~1e22g due to finite source and wave optics effects, which makes it challenging to detect any microlensing events due to lenses with masses <~1e22g (see e.g. Fig. 7 of Sugiyama et al. (2020) [1905.06066])

- Compare to the extended MF constraints obtained only including f_max < 1 (solid lines)

Results:
- The difference from the results including only f_ max < 1 from the power-law extrapolations is barely visible at the upper end of the asteroid-mass window
- At the upper end of the asteroid-mass window, the difference from including only f_max < 1 and the case where f_max is extrapolated below 9e21g using a power law with exponent -2 is:
- Delta = 0: approximately 20% for the SLN, CC3 and LN
- Delta = 5: approximately 7% for the SLN, CC3 and LN

Conclusion:
I will use the results obtained using f_max < 1 only, since the difference from the results obtained using a power-law extrapolation is small.

Prospective Constraints

Future MeV-gamma ray telescopes (Fig. 8 of 2101.01370, GECCO)

Results shown are for the Einasto profile (tightest constraint)
Since these are photon constraints, the most reasonable PL exponent is probably between 2 and 3. The exponents showing values of 0 and 4 are more extreme test cases.

Maximum differences at the lower end of the asteroid-mass window:
- Differences between exponents of 0 and 2 are < 1%
- Differences between exponents of 2 and 4 are (for Delta=5):
  - ~1% (SLN)
  - ~5% (CC3)
  - ~4% (LN): note that this does not quite reach f_PBH = 1, due to the width of the mass function being too wide
From this, I would conclude the differences are unimportant.
The most reasonable value of these is the PL slope of 2, so I will use this plotted going forward

27/7

Check
Compare results obtained at t=0 (with the ‘evolved’ MF) to the unevolved MF
Check passed:
- Differences are not visible at any Delta
- Differences are < 5% for all Delta

Prospective microlensing constraints from white dwarf survey
Delta-function MF constraints are shown in Fig. 8 of Sugiyama et al. (2020) [1905.06066]

Thoughts on the constraining power of the region where f_max > 1:
- Due to the constraint being very steep at the lower cut-off (which arises from wave optics effects), the constraining power for masses m <~2.5e-12 M_\odot is likely insignificant
  - Compared to Subaru-HSC constraints from Croon et al. (2020), the prospective constraint is much steeper (almost vertical)
  - I found that the effect of using a power-law to extrapolate the Subaru-HSC delta-function MF constraint to lower masses on the extended MF constraint is fairly small
  - Therefore, it seems reasonable to assume that a similar treatment describing f_max where f_max > 1 would have a small effect on the resulting extended MF constraints

Therefore, only consider the mass range where f_max < 1

Convergence tests for KP ‘23 constraints:

To check (for degree of convergence)

1) Number of values of the initial mass to evaluate the evolved MF at
In preliminaries.py, add an optional argument to constraints_Carr() (“n_steps”) which controls the number of evolved masses to evaluate the evolved MF at:

def constraint_Carr(mc_values, m_delta, f_max, psi_initial, params, evolved=True, t=t_0, n_steps=1000):

…
so that the initial masses are given by

        m_init_values_input = np.sort(np.concatenate((np.logspace(np.log10(min(m_delta)), np.log10(m_star), n_steps), np.arange(m_star, m_star*(1+1e-11), 5e2), np.arange(m_star*(1+1e-11), m_star*(1+1e-6), 1e7), np.logspace(np.log10(m_star*(1+1e-4)), np.log10(max(m_delta))+4, n_steps))))

Vary this number between [1e3, 1e4, 1e5] bold = default value used in other plots

2) Power-law extrapolation to small masses in the delta-function MF constraint
When using a power-law in f_max(M), change the minimum mass at which the delta-function MF constraint is evaluated at

NOTE: Keep the spacing between masses that the delta-function MF constraint is evaluated at constant, while varying the range over which the delta-function MF constraint is evaluated at.

Vary this number between [1e7g, 1e9g, 1e11g] bold = default value used in other plots

Results
Sanity check:
- checked the Delta = 5 results match reasonably well with those from the test comparing results with power-law extrapolations of the delta-function MF constraint down to 1e11g

Plot the results for all three cases in plot_constraints_tests.py
See the cell “Convergence test with number of masses in preliminaries.py and range of masses included in power-law extrapolation of the delta-function MF constraint. Consider the evolved MFs only, with PL extrapolation.”

Difference between results for f_PBH obtained using defaults and using more precise calculations (in the peak mass range m_p > 1e16g, with f_PBH < 1):
  - Not visible in any case (SLN, CC3 or LN)
    - Difference between results with n_steps = 1e3 and n_steps = 1e4 steps is no more than ~1 part in 10^4
    - Difference between minimum mass of PL extrapolation even smaller